Enabler Test Specification for Lightweight M2M

Draft Version 1.0 – 17 Oct 2013

Open Mobile Alliance

OMA-ETS-LightweightM2M-V1_0-20131017-D

Use of this document is subject to all of the terms and conditions of the Use Agreement located at http://www.openmobilealliance.org/UseAgreement.html.

Unless this document is clearly designated as an approved specification, this document is a work in process, is not an approved Open Mobile Alliance™ specification, and is subject to revision or removal without notice.

You may use this document or any part of the document for internal or educational purposes only, provided you do not modify, edit or take out of context the information in this document in any manner.  Information contained in this document may be used, at your sole risk, for any purposes.  You may not use this document in any other manner without the prior written permission of the Open Mobile Alliance.  The Open Mobile Alliance authorizes you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms.  This copyright permission does not constitute an endorsement of the products or services.  The Open Mobile Alliance assumes no responsibility for errors or omissions in this document.

Each Open Mobile Alliance member has agreed to use reasonable endeavors to inform the Open Mobile Alliance in a timely manner of Essential IPR as it becomes aware that the Essential IPR is related to the prepared or published specification.  However, the members do not have an obligation to conduct IPR searches.  The declared Essential IPR is publicly available to members and non-members of the Open Mobile Alliance and may be found on the “OMA IPR Declarations” list at http://www.openmobilealliance.org/ipr.html.  The Open Mobile Alliance has not conducted an independent IPR review of this document and the information contained herein, and makes no representations or warranties regarding third party IPR, including without limitation patents, copyrights or trade secret rights.  This document may contain inventions for which you must obtain licenses from third parties before making, using or selling the inventions.  Defined terms above are set forth in the schedule to the Open Mobile Alliance Application Form.

NO REPRESENTATIONS OR WARRANTIES (WHETHER EXPRESS OR IMPLIED) ARE MADE BY THE OPEN MOBILE ALLIANCE OR ANY OPEN MOBILE ALLIANCE MEMBER OR ITS AFFILIATES REGARDING ANY OF THE IPR’S REPRESENTED ON THE “OMA IPR DECLARATIONS” LIST, INCLUDING, BUT NOT LIMITED TO THE ACCURACY, COMPLETENESS, VALIDITY OR RELEVANCE OF THE INFORMATION OR WHETHER OR NOT SUCH RIGHTS ARE ESSENTIAL OR NON-ESSENTIAL.

THE OPEN MOBILE ALLIANCE IS NOT LIABLE FOR AND HEREBY DISCLAIMS ANY DIRECT, INDIRECT, PUNITIVE, SPECIAL, INCIDENTAL, CONSEQUENTIAL, OR EXEMPLARY DAMAGES ARISING OUT OF OR IN CONNECTION WITH THE USE OF DOCUMENTS AND THE INFORMATION CONTAINED IN THE DOCUMENTS.

© 2013 Open Mobile Alliance Ltd.  All Rights Reserved.
Used with the permission of the Open Mobile Alliance Ltd. under the terms set forth above.

Contents

1.	Scope	4

2.	References	5

2.1	Normative References	5

2.2	Informative References	5

3.	Terminology and Conventions	6

3.1	Conventions	6

3.2	Definitions	6

3.3	Abbreviations	7

4.	Introduction	8

5.	LightweightM2M Conformance Test Cases	9

6.	LightweigthM2M Interoperability Test Cases	10

6.1	Registration	10

6.11	LightweightM2M-1.0-int-101 – Initial Registration	10

6.12	LightweightM2M-1.0-int-102 – Registration Update	10

6.13	LightweightM2M-1.0-int-103 – Deregistration	11

6.2	Device object-related use cases	11

6.21	LightweightM2M-1.0-int-201 – Querying basic information from the client	11

6.22	LightweightM2M-1.0-int-202 – Querying the firmware version from the client	12

6.23	LightweightM2M-1.0-int-203 – Rebooting the device	12

6.24	LightweightM2M-1.0-int-204 – Querying power status of the terminal	13

6.3	Device firmware update	13

6.31	LightweightM2M-1.0-int-301 – Firmware update (via COAP)	13

6.32	LightweightM2M-1.0-int-302 – Firmware update (via alternative mechanism)	14

6.4	Connectivity object monitoring	15

6.41	LightweightM2M-1.0-int-401 – Querying of connectivity parameters	15

6.5	Observe and Notify	16

6.51	LightweightM2M-1.0-int-501 – Observation and notification of parameter values inside MachineLink 3G	16

Appendix A.	Change History (Informative)	17

A.1	Approved Version History	17

A.2	Draft/Candidate Version 1.0 History	17

Appendix B.	Additional Information	18

B.1	Example of Test Configuration and Setup	18

# Scope

This document describes in detail available test cases for LightweigthM2M as specified in OMA-TS-LightweightM2M-V1_0-20130616-D.

The test cases are split in two categories, conformance and interoperability test cases.

The conformance test cases are aimed to verify the adherence to normative requirements described in the technical specifications.

The interoperability test cases are aimed to verify that implementations of the specifications work satisfactory.

If either conformance or interoperability tests do not exists at the creation of the test specification this part should be marked not available.

# References

## Normative References

| [3GPP-TS_23.003] | 3GPP TS 23.003 “Numbering, addressing and identification” |
| --- | --- |
| [CoAP] | Shelby, Z., Hartke, K., Bormann, C., and B. Frank, "Constrained Application Protocol (CoAP)", draft-ietf-core-coap-14 (work in progress), Mar 2013. |
| [ETSI TS 102.221] | “Smart Cards; UICC-Terminal interface; Physical and logical characteristics”, (ETSI TS 102 221 release 11), URL:http://www.etsi.org/ |
| [GlobalPlatform SCP 02] | GlobalPlatform v2.2.1 - January 2011 - Appendix E : Secure Channel Protocol 02 (SCP 02) |
| [IOPPROC] | “OMA Interoperability Policy and Process”, Version 1.1, Open Mobile Alliance™, OMA-IOP-Process-V1_1, URL:http://www.openmobilealliance.org/ |
| [LWM2M-AD] | “Lightweight Machine to Machine Architecture”, Open Mobile Alliance™, OMA-AD-LightweightM2M-V1_0, URL:http://www.openmobilealliance.org/ |
| [OBSERVE] | Hartke, K. “Observing Resources in CoAP”, draft-ietf-core-observe-08 (work in progress), Mar 2013. |
| [PKCS#15] | PKCS #15 v1.1: Cryptographic Token Information Syntax Standard”, RSA Laboratories, June 6, 2000. URL: ftp://ftp.rsasecurity.com/pub/pkcs/pkcs-15/pkcs-15v1_1.pdf |
| [RFC2119] | “Key words for use in RFCs to Indicate Requirement Levels”, S. Bradner, March 1997, URL:http://www.ietf.org/rfc/rfc2119.txt |
| [RFC2234] | “Augmented BNF for Syntax Specifications: ABNF”. D. Crocker, Ed., P. Overell. November 1997, URL:http://www.ietf.org/rfc/rfc2234.txt |
| [RFC4122] | “A Universally Unique Identifier (UUID) URN Namespace”, P. Leach, et al. July 2005, URL:http://www.ietf.org/rfc/rfc4122.txt |
| [RFC5246] | The Transport Layer Security (TLS) Protocol Version 1.2 |
| [RFC5289] | TLS Elliptic Curve Cipher Suites with SHA-256/384 and AES Galois Counter Mode (GCM) |
| [RFC5487] | Pre-Shared Key Cipher Suites for TLS with SHA-256/384 and AES Galois Counter Mode |
| [RFC6347] | Rescorla, E. and N. Modadugu, "Datagram Transport Layer Security Version 1.2", RFC 6347, January 2012. |
| [RFC6655] | McGrew, D. and D. Bailey, "AES-CCM Cipher Suites for TLS", RFC6655, July 2012. |
| [RFC6690] | Shelby, Z. “Constrained RESTful Environments (CoRE) Link Format”, RFC6690, Aug 2012. |

## Informative References

| [DMREPPRO] | “OMA Device Management Representation Protocol, Version 1.3”. Open Mobile Alliance(. OMA-TS-DM_RepPro-V1_3. URL:http://www.openmobilealliance.org |
| --- | --- |
| [OMADICT] | “Dictionary for OMA Specifications”, Version 2.9, Open Mobile Alliance™, OMA-ORG-Dictionary-V2_9, URL:http://www.openmobilealliance.org/ |

# Terminology and Conventions

## Conventions

The key words “MUST”, “MUST NOT”, “REQUIRED”, “SHALL”, “SHALL NOT”, “SHOULD”, “SHOULD NOT”, “RECOMMENDED”, “MAY”, and “OPTIONAL” in this document are to be interpreted as described in [RFC2119].

All sections and appendixes, except “Scope”, are normative, unless they are explicitly indicated to be informative.

The following numbering scheme is used:

xxx-y.z-con-number where:
xxx	Name of enabler, e.g. MMS or Browsing
y.z	Version of enabler release, e.g. 1.2 or 1.2.1
’con’	Indicating this test is a conformance test case
number	Leap number for the test case

Or

xxx-y.z-int-number where:
xxx	Name of enabler, e.g. MMS or Browsing
y.z	Version of enabler release, e.g. 1.2 or 1.2.1
’int’	Indicating this test is a interoperability test case
number	Leap number for the test case

## Definitions

| Application Device Module | 1) The customer's realisation of a service through M2M - e.g. satnav, smart metering 2) Individual software components that run on top of the device's operating system.Access Point Name The hardware that is realising a function for the customer e.g. a smart meter. A modular component of a device e.g. the radio module housing the SIM |
| --- | --- |

## Abbreviations

| API APN CON DM GDSP GUI IMEI IMSI IOP LWM2M M2M MSISDN OMA OpCo OS SIM UI | Application Programming Interface Access Point Name Conformance Device Management Global Data Service Platform Graphical User Interface International Mobile Equipment Identity International Mobile Subscriber Identity Interoperability Lightweight Machine to Machine (refers to this OMA enabler) Machine to Machine Mobile Station International Subscriber Directory Number Open Mobile Alliance Operating Company Operating System Subscriber Interface Module User Interface |
| --- | --- |

# Introduction

The purpose of this document is to provide test cases for LightweigthM2M Enabler Release V1.0.

The implementation of some features is optional for the Clients and/or the Servers in the LightweigthM2M Enabler.  The tests associated with these optional features are marked as "(Includes Optional Features)" in the test specification.

The following items on an overall level are needed to adequately test the LWM2M enabler:

- A LWM2M server

- A LWM2M client e.g. embedded in a M2M device or module connected via UDP and SMS with the LWM2M server

The LWM2M enabler tests are carried out using the LWM2M protocol and objects, and using the underlying protocols such as [CoAP].

# LightweightM2M Conformance Test Cases

tbd

# LightweigthM2M Interoperability Test Cases

## Registration

## LightweightM2M-1.0-int-101 – Initial Registration

| Test Case Id | LightweigthM2M-1.0-int-101 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Test that the Client registers with the Server. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is turned on The bootstrap procedure has been completed or the required bootstrap information is available to the client The client has a LWM2M Server Object Instance. |
| Test Procedure | Device is switched on and bootstrap information is available to the device. The device automatically registers at the server, once this information is available. Normal flow: a. Registration message (COAP POST) is sent from client to server. b. Client receives Success message (2.01 Created) from the server. |
| Pass-Criteria | Server has received REGISTER operation Server knows the following Endpoint Client Name registration lifetime (optional) LWM2M version (optional) binding mode (optional) SMS number (optional) Objects and Object Instances (optional) Client has received “Success” message from server |

## LightweightM2M-1.0-int-102 – Registration Update

| Test Case Id | LightweigthM2M-1.0-int-102 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Test that the client updates the registration information on the server. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Need exists to re-register, e.g. previous registration has expired. |
| Test Procedure | 1. Switch on device and try to Re-Register Normal flow: a. Re-Registration message (COAP PUT) is sent from client to server. b. Client receives Success message (2.04 Changed) from the server. |
| Pass-Criteria | 1. Server has received REGISTER operation 2. Server knows the following Endpoint Client Name registration lifetime (optional) LWM2M version (optional) binding mode (optional) SMS number (optional) Objects and Object Instances (optional) 3. Client has received “Success” message from server |

## LightweightM2M-1.0-int-103 – Deregistration

| Test Case Id | LightweigthM2M-1.0-int-103 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Test that the client is able to deregister at the server. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Client is registered |
| Test Procedure | 1. Client will no longer be available, thus, it should de-register Normal flow: a. Deregistration message (COAP delete) is sent from client to server. b. Client receives Success message (2.02 Deleted) from the server. |
| Pass-Criteria | 1. Client is removed from the servers registration data base |

## Device object-related use cases

## LightweightM2M-1.0-int-201 – Querying basic information from the client

| Test Case Id | LightweigthM2M-1.0-int-201 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Querying the following data on the client: Manufacturer Model number Serial number. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered at the LWM2M server |
| Test Procedure | A READ operation from server on these resources has been received by the client. Normal flow: a. READ (COAP GET) on device object resources. b. Client receives success message (2.05 Content) and the requested values in the corresponding Plain Text, TLV or JSON format. |
| Pass-Criteria | Server has received the requested information and display of the following data to the user is possible: Manufacturer Model number Serial number |

## LightweightM2M-1.0-int-202 – Querying the firmware version from the client

| Test Case Id | LightweigthM2M-1.0-int-202 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Querying the firmware version of the firmware on the managed device |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered with the Server |
| Test Procedure | A READ operation from server on the resource has been received by the client. Normal flow: a. READ (COAP GET) on device object resource “firmware version” b. Client receives success message (2.05 Content) and the requested value in the corresponding Plain Text format. |
| Pass-Criteria | Server has received the requested information and displays to the user the following information: Firmware version |

## LightweightM2M-1.0-int-203 – Rebooting the device

| Test Case Id | LightweigthM2M-1.0-int-203 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Test that rebooting of the device remotely through the server is possible. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is switched on and registered with the server. (Device might be in a state that requires a reboot) |
| Test Procedure | An EXECUTE operation from server on the resource object/reboot has been received by the client. Normal flow: a. Server performs Execute (COAP POST) on device/reboot resource b. Client receives success message (2.04 Changed) from server |
| Pass-Criteria | Device reboots successfully and re-registers at the server again |

## LightweightM2M-1.0-int-204 – Querying power status of the terminal

| Test Case Id | LightweigthM2M-1.0-int-204 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Test that you can query the device for its power status (e.g. on battery or on mains) and/or for the voltage level of its power supply. |
| Tool | Device Hardware |
| Test code | n/a |
| Preconditions | Device is registered with the LWM2M server. Device is operational and connected to some power supply |
| Test Procedure | A READ operation from server on these resources is received by the client. Normal flow: a. READ (COAP GET) on the following device object resources related to power status: Available Power Sources Battery level Power Source Voltage Power Source Current b. Client receives success message (2.05 Content) and the requested values in the corresponding TLV or JSON format |
| Pass-Criteria | Available Power Source status and Battery level are available on the server and can be displayed. Voltage and current level of the power supply to the device is available on the server and can be displayed. |

## Device firmware update

## LightweightM2M-1.0-int-301 – Firmware update (via COAP)

| Test Case Id | LightweigthM2M-1.0-int-301 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Perform a device firmware update remotely triggered by the LWM2M server. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered at the LWM2M server Device is switched on and operational. Firmware Update is available on the Server |
| Test Procedure | A WRITE operation from the server on firmware/package is received by the client Normal flow: a. The server delivers the firmware to the device through a WRITE operation on firmware/package b. A READ on firmware/state provides the status of the firmware download to the server c. The server may send repeated READs to determine when the download is completed. d. If the downloaded is completed, the server initiates a firmware update by EXECUTE firmware/update e. The device is rebooting. f. The server READs the result of the firmware update procedure. |
| Pass-Criteria | New firmware is installed on the device. The device is rebooted. The server receives the status code “1” for success. |

## LightweightM2M-1.0-int-302 – Firmware update (via alternative mechanism)

| Test Case Id | LightweigthM2M-1.0-int-302 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Perform a device firmware update remotely triggered by the LWM2M server. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered at the LWM2M server Device is switched on and operational. Firmware Update is available on the Server |
| Test Procedure | 1. A WRITE operation from the server on firmware/package URI is received by the client Normal flow: The server delivers the firmware URI to the device through a WRITE operation on firmware/URI The device downloads the firmware from the URI via an alternative mechanism (not COAP) c. A READ on firmware/state provides the status of the firmware download to the server d. The server may send repeated READs to determine when the download is completed. e. If the downloaded is completed, the server initiates a firmware update by EXECUTE firmware/update e. The device is rebooting. f. The server READs the result of the firmware update procedure. |
| Pass-Criteria | 1. New firmware is installed on the device. 2. The device reboots. 3. The server receives the status code “1” for success. |

## Connectivity object monitoring

## LightweightM2M-1.0-int-401 – Querying of connectivity parameters

| Test Case Id | LightweigthM2M-1.0-int-401 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Querying multiple parameters related to connectivity on the device. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered at the LWM2M server Device is switched on and operational. |
| Test Procedure | A READ operation from server on the following resources has been received by the client: Network bearer (used) Available network bearer Signal Strength Link quality Service mobile network code Country code Cell ID APN IP address of the device |
| Pass-Criteria | The server has received the requested information and display to the user is possible. |

## Observe and Notify

## LightweightM2M-1.0-int-501 – Observation and notification of parameter values inside MachineLink 3G

| Test Case Id | LightweigthM2M-1.0-int-501 |
| --- | --- |
| Test Object | Client and Server |
| Test Case Description | Sending the observation policy to the device. |
| Tool | n/a |
| Test code | n/a |
| Preconditions | Device is registered at the LWM2M server Device is switched on and operational. |
| Test Procedure | A WRITE operation from the server is received by the client requesting: Line Voltage Signal Strength Normal flow: a. Server communicates to the device min/max period, threshold value and step with a WRITE ATTRIBUTE operation b. Server sends OBSERVE message to activate reporting c. Client reports requested information with a NOTIFY message |
| Pass-Criteria | The server has received the requested information and display of “Line Voltage” and “Signal Strength” to the user is possible. |

Change History	(Informative)

Approved Version History

| Reference | Date | Description |
| --- | --- | --- |
| n/a | n/a | No prior version |

Draft/Candidate Version 1.0 History

| Document Identifier | Date | Sections | Description |
| --- | --- | --- | --- |
| Draft Versions OMA-ETS-LightweightM2M-V1_0 | 18 Jun 2013 | All | First Draft as agreed in OMA-IOP-MEC-2013-0083-INP_ETS_for_LWM2M |
|  | 17 Oct 2013 | All | Cleaned up Version for the LWM2M Testfest in Las Vegas as agreed in OMA-IOP-MEC-2013-0103-CR_Clean_up_of_LWM2M_ETS |

Additional Information

Example of Test Configuration and Setup

The following hardware components were part of a test setup.

- M2M device equipped with LWM2M client

- Computer that runs the browser interface to the LWM2M server component

- Server that runs the LWM2M server software

- USIM provisioned for use on the network.

- External appliance which is connected directly to M2M device (e.g. light, temperature sensor, motor).

In addition the demonstration setup shall include the following software components:

- Measurement software which enables to see e.g. LWM2M messages and CoAP messages.

- The software shall enable

- GUI to trigger the chosen test cases

- To see the flow of information between client and server, e.g. on LWM2M protocol level and on CoAP transport level.