SyncML OBEX Binding

Approved Version 1.2 – 21 Feb 2007

Open Mobile Alliance

OMA-TS-SyncML_OBEXBinding-V1_2-20070221-A

Use of this document is subject to all of the terms and conditions of the Use Agreement located at http://www.openmobilealliance.org/UseAgreement.html.

Unless this document is clearly designated as an approved specification, this document is a work in process, is not an approved Open Mobile Alliance™ specification, and is subject to revision or removal without notice.

You may use this document or any part of the document for internal or educational purposes only, provided you do not modify, edit or take out of context the information in this document in any manner.  Information contained in this document may be used, at your sole risk, for any purposes.  You may not use this document in any other manner without the prior written permission of the Open Mobile Alliance.  The Open Mobile Alliance authorizes you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms.  This copyright permission does not constitute an endorsement of the products or services.  The Open Mobile Alliance assumes no responsibility for errors or omissions in this document.

Each Open Mobile Alliance member has agreed to use reasonable endeavors to inform the Open Mobile Alliance in a timely manner of Essential IPR as it becomes aware that the Essential IPR is related to the prepared or published specification.  However, the members do not have an obligation to conduct IPR searches.  The declared Essential IPR is publicly available to members and non-members of the Open Mobile Alliance and may be found on the “OMA IPR Declarations” list at http://www.openmobilealliance.org/ipr.html.  The Open Mobile Alliance has not conducted an independent IPR review of this document and the information contained herein, and makes no representations or warranties regarding third party IPR, including without limitation patents, copyrights or trade secret rights.  This document may contain inventions for which you must obtain licenses from third parties before making, using or selling the inventions.  Defined terms above are set forth in the schedule to the Open Mobile Alliance Application Form.

NO REPRESENTATIONS OR WARRANTIES (WHETHER EXPRESS OR IMPLIED) ARE MADE BY THE OPEN MOBILE ALLIANCE OR ANY OPEN MOBILE ALLIANCE MEMBER OR ITS AFFILIATES REGARDING ANY OF THE IPR’S REPRESENTED ON THE “OMA IPR DECLARATIONS” LIST, INCLUDING, BUT NOT LIMITED TO THE ACCURACY, COMPLETENESS, VALIDITY OR RELEVANCE OF THE INFORMATION OR WHETHER OR NOT SUCH RIGHTS ARE ESSENTIAL OR NON-ESSENTIAL.

THE OPEN MOBILE ALLIANCE IS NOT LIABLE FOR AND HEREBY DISCLAIMS ANY DIRECT, INDIRECT, PUNITIVE, SPECIAL, INCIDENTAL, CONSEQUENTIAL, OR EXEMPLARY DAMAGES ARISING OUT OF OR IN CONNECTION WITH THE USE OF DOCUMENTS AND THE INFORMATION CONTAINED IN THE DOCUMENTS.

© 2007 Open Mobile Alliance Ltd.  All Rights Reserved.
Used with the permission of the Open Mobile Alliance Ltd. under the terms set forth above.

Contents

1.	Scope	5

2.	References	6

2.1	Normative References	6

2.2	Informative References	6

3.	Terminology and Conventions	7

3.1	Conventions	7

3.2	Definitions	7

3.3	Abbreviations	8

4.	Introduction	9

5.	OBEX Introduction	10

5.1	OBEX Over IrDA	10

5.1.1	IAS Entry	11

5.2	OBEX Over Bluetooth	12

5.2.1	Bluetooth Service Discovery	12

5.2.2	Other Bluetooth Protocol Requirements	14

6.	OBEX Mapping to SyncML	15

6.1	OBEX Operations	15

6.2	OBEX Connection Overview	16

6.2.1	Multiple Messages Per Package	16

6.2.2	Type header requirement	17

6.3	OBEX Connection Establishment	17

6.4	Exchanging SyncML Data over the OBEX Connection	18

6.5	OBEX Disconnection	20

6.6	OBEX ABORT	21

6.7	Server Alerted Notification	21

7.	Examples	23

7.1	OBEX Connect Example	23

7.2	OBEX Disconnect Example	24

7.3	OBEX Abort Example	24

7.4	OBEX Put Example	24

7.5	OBEX Get Example	26

Appendix A.	Change History (Informative)	28

A.1	Approved Version History	28

A.2	Draft/Candidate Version 1.2 History	Error! Bookmark not defined.

Appendix B.	Static Conformance Requirements (Normative)	29

B.1	Client Features	29

B.1.1	Common SCRs – OBEX Session Requirements	29

B.1.2	SCRs for Client Initiated Sessions	29

B.1.3	SCRs for Server Initiated Sessions	29

B.2	Server Features	29

B.2.1	Common SCRs	29

B.2.2	SCRs for Client Initiated Sessions	29

B.3	SCRs for Server Initiated Sessions	30

Figures

Figure 1 OBEX over Bluetooth	12

Tables

Table 1 SyncML Server Service Records	13

Table 2 SyncML Client Service Records	13

Table 3 SDP PDUs	14

# Scope

The SyncML Initiative, Ltd. was a not-for-profit corporation formed by a group of companies who co-operated to produce an open specification for data synchronization and device management. Prior to SyncML, data synchronization and device management had been based on a set of different, proprietary protocols, each functioning only with a very limited number of devices, systems and data types. These non-interoperable technologies have complicated the tasks of users, manufacturers, service providers, and developers. Further, a proliferation of different, proprietary data synchronization and device management protocols has placed barriers to the extended use of mobile devices, has restricted data access and delivery and limited the mobility of the users.

SyncML is a specification that contains the following main components:

- An XML-based representation protocol

- A synchronization protocol and a device management protocol

- Transport bindings for the protocol

The data representation specifies an XML DTD that allows the representation of all the information required to perform synchronization or device management, including data, metadata and commands. The synchronization and device management protocols specify how SyncML messages conforming to the DTD are exchanged in order to allow a SyncML client and server to exchange additions, deletes, updates and other status information.

There are also DTDs which define the representation of information about the device such as memory capacity, and the representation of various types of meta information such as security credentials.

Although the SyncML specification defines transport bindings that specify how to use a particular transport to exchange messages and responses, the SyncML representation, synchronization and device management protocols are transport-independent. Each SyncML package is completely self-contained, and could in principle be carried by any transport. The initial bindings specified are HTTP, WSP and OBEX, but there is no reason why SyncML could not be implemented using email or message queues, to list only two alternatives. Because SyncML messages are self-contained, multiple transports may be used without either the server or client devices having to be aware of the network topology. Thus, a short-range OBEX connection could be used for local connectivity, with the messages being passed on via HTTP to an Internet-hosted synchronization server.

To reduce the data size, a binary coding of SyncML based on the WAP Forum's WBXML is defined. Messages may also be passed in clear text if required. In this and other ways SyncML addresses the bandwidth and resource limitations imposed by mobile devices.

SyncML is both data type and data store independent. SyncML can carry any data type which can be represented as a MIME object. To promote interoperability between different implementations of SyncML, the specification includes the representation formats used for common PIM data.

This document describes how to use SyncML over OBEX. The document uses the primitives and methods defined in the OBEX specification V1.2 as defined in [OBEX]

# References

## Normative References

| [BTAN] | “Bluetooth Assigned Numbers”, Bluetooth SIG, URL: http://www.bluetoothsig.org/assigned-numbers/ |
| --- | --- |
| [BTGOEP] | “Bluetooth V1.1 Profile Specifications” – PartK:10 Generic Object Exchange Profile, Bluetooth SIG, URL: http://www.bluetooth.org/foundry/specification/document/Bluetooth_11_Profiles_Book/en/1/Bluetooth_11_Profiles_Book.pdf |
| [BTSDP] | “Bluetooth V1.1 Core Specifications” - PartE: Service Discovery Protocol, Bluetooth SIG, URL: http://www.bluetooth.org/foundry/specification/document/Bluetooth_V1.1_Core_Specifications/en/1/Bluetooth_V1.1_Core_Specifications.pdf |
| [BTSEP] | “Bluetooth V1.1 Profile Specifications” – PartK:5 Serial Port Profile, Bluetooth SIG, URL: http://www.bluetooth.org/foundry/specification/document/Bluetooth_11_Profiles_Book/en/1/Bluetooth_11_Profiles_Book.pdf |
| [IOPPROC] | “OMA Interoperability Policy and Process”, Version 1.1, Open Mobile Alliance™, OMA-IOP-Process-V1_1, URL:http://www.openmobilealliance.org/ |
| [OBEX] | “IrDA Object Exchange Protocol (IrOBEX) Version 1.2”, Infrared Data Association, URL: http://www.irda.org/standards/pubs/OBEX1p2_Plus.zip |
| [RFC2119] | “Key words for use in RFCs to Indicate Requirement Levels”, S. Bradner, March 1997, URL:http://www.ietf.org/rfc/rfc2119.txt |
| [RFC2396] | “Uniform Resource Identifiers (URI): Generic Syntax”, T. Berners-Lee, et al., August 1998, URL:http://www.ietf.org/rfc/rfc2396.txt |
| [SAN] | “SyncML Server Alerted Notification”, Open Mobile AllianceTM , OMA-TS-SyncML_SAN-V1_2, URL:http://www.openmobilealliance.org/ |

## Informative References

| None. |  |
| --- | --- |

# Terminology and Conventions

## Conventions

The key words “MUST”, “MUST NOT”, “REQUIRED”, “SHALL”, “SHALL NOT”, “SHOULD”, “SHOULD NOT”, “RECOMMENDED”, “MAY”, and “OPTIONAL” in this document are to be interpreted as described in [RFC2119].

All sections and appendixes, except “Scope” and “Introduction”, are normative, unless they are explicitly indicated to be informative.

Any reference to components of the SyncML DTD or XML snippets is specified in this typeface.

## Definitions

| Application | A SyncML application that supports the SyncML protocol. The application can either be the originator or recipient of the SyncML protocol commands. The application can act as a SyncML client or a SyncML server. |
| --- | --- |
| Capabilities exchange | The SyncML capability that allows a client and server to exchange what device, user and application features they each support. |
| Client | A SyncML Client refers to the protocol role when the application issues SyncML "request" messages. For example in data synchronization, the Sync SyncML Command in a SyncML Message. |
| Command | A SyncML Command is a protocol primitive. Each SyncML Command specifies to a recipient an individual operation that is to be performed. For example, the SyncML Commands supported by this specification include Add, Alert, Atomic, Copy, Delete, Exec, Get, Map, Replace, Search, Sequence and Sync. |
| Data | A unit of information exchange, encoded for transmission over a network. |
| Data collection | A data element which acts as a container of other data elements, (e.g., {c {{i1, data1}, ... {in, datan}}}). In SyncML, data collections are synchronized with each other. See data element |
| data element | A piece of data and an associated identifier for the data, (e.g., {i, data}). |
| Data element equivalence | When two data elements are synchronized. The exact semantics is defined by a given data synchronization model. |
| Data exchange | The act of sending, requesting or receiving a set of data elements. |
| Data format | The encoding used to format a data type. For example, characters or integers or character encoded binary data. |
| Data type | The schema used to represent a data object (e.g., text/calendar MIME content type for an iCalendar representation of calendar information or text/directory MIME content type for a vCard representation of contact information). |
| Data synchronization | The act of establishing an equivalence between two data collections, where each data element in one item maps to a data item in the other, and their data is equivalent. |
| Data synchronization protocol | The well-defined specification of the "handshaking" or workflow needed to accomplish synchronization of data elements on an originator and recipient data collection. The SyncML specification forms the basis for specifying an open data synchronization protocol. |
| Message | A SyncML Message is the primary contents of a SyncML Package. It contains the SyncML Commands, as well as the related data and meta-information. The SyncML Message is an XML document. |
| OBEX | Objext Exchange Protocol that is defined in [OBEX] . |
| Operation | A SyncML Operation refers to the conceptual transaction achieved by the SyncML Commands specified by a SyncML Package. For example in the case of data synchronization, "synchronize my personal address book with a public address book". |
| Originator | The network device that creates a SyncML request. |
| Package | A SyncML Package is the complete set of commands and related data elements that are transferred between an originator and a recipient. The SyncML package can consist of one or more SyncML Messages. |
| Parser | Refers to an XML parser. An XML parser is not absolutely needed to support SyncML. However, a SyncML implementation that integrates an XML parser might be easier to enhance. This document assumes that the reader has some familiarity with XML syntax and terminology. |
| Recipient | The network device that receives a SyncML request, processes the request and sends any resultant SyncML response. |
| Representation protocol | A well-defined format for exchanging a particular form of information. SyncML is a representation protocol for conveying data synchronization and device management operations. |
| Server Alerted Notification | The method by which a SyncML server can notify a SyncML client to initiate a SyncML session |
| SyncML request message | An initial SyncML Message that is sent by an originator to a recipient network device. |
| SyncML response message | A reply SyncML Message that is sent by a recipient of a SyncML Request back to the originator of the SyncML Request |
| Synchronization data | Refers to the data elements within a SyncML Command. In a general reference, can also refer to the sum of the data elements within a SyncML Message or SyncML Package. |
| Server | A SyncML Server refers to the protocol role when an application issues SyncML "response" messages. For example in the case of data synchronization, a Results Command in a SyncML Message. |

## Abbreviations

| OMA | Open Mobile Alliance |
| --- | --- |
| URI | Uniform Resource Identifier [RFC2396] |
| URL | Uniform Resource Locator [RFC2396] |
| WAP | Wireless Application Protocol |
| XML | Extensible Markup Language |

# Introduction

This document describes how to use the SyncML over OBEX. The document uses the primitives and methods defined in the OBEX specification V1.2  [OBEX] .

The document assumes a scenario consisting of a SyncML client (e.g. a mobile phone) and a server holding data.  The OBEX transport was originally used over short-range links like infrared.  With short-range links, the SyncML server could be a local PC.  With wide area networks, the SyncML server could be a remote WEB server.

# OBEX Introduction

OBEX [OBEX]  is a protocol for exchanging objects.  It was initially designed for infrared, but it has been adopted by Bluetooth, and is also used over RS232, USB and WAP.

OBEX is a session-oriented protocol, which allows multiple request/response exchanges in one session. An OBEX session is initiated by an OBEX CONNECT request, and is established when the other device returns a success response.  The connection is terminated by sending a DISCONNECT request.

In this specification, the SyncML client can work either as an OBEX client or as an OBEX server at the OBEX protocol layer. In consequence, the SyncML server can work either as an OBEX client or as an OBEX server. The OBEX role depends on the fact which one, the SyncML client or the SyncML server, initiates sync. Thus the SyncML Client is not necessarily the OBEX Client.

When a session has been established, the data is transferred using the PUT request.  The remote device acknowledges the data, by sending a response with a status code.

SyncML requires that an OBEX connection is established.  Connectionless OBEX cannot be used with SyncML.

## OBEX Over IrDA

The diagram below demonstrates the position of OBEX within the IrDA stack.

IrLAP is the link level protocol.

IrLMP is a multiplexing layer.

Tiny TP provides flow control.

IAS is the Information Access Service.

OBEX includes both a session level protocol and an application framework.

### IAS Entry

To enable an OBEX connection over IrDA, the OBEX protocol stack needs to provide IAS setting information to the IAS protocol stack.  The SyncML server and SyncML client SHOULD use the following IAS entry settings for SyncML communication via OBEX over IrDA.

#### IAS Entry Settings for SyncML Server

SyncML server SHOULD use the following IAS entry settings.

| Class | OBEX:SyncML-Server |
| --- | --- |
| Attribute | Name | IrDA:TinyTP:LsapSel |
|  | Type | Integer |
|  | Description | IrLMP LSAP selector for SyncML over IrOBEX, legal values from 0x01 to 0x6F |

#### IAS Entry Settings for SyncML Client

SyncML client SHOULD use the following IAS entry settings.

| Class | OBEX:SyncML-Client |
| --- | --- |
| Attribute | Name | IrDA:TinyTP:LsapSel |
|  | Type | Integer |
|  | Description | IrLMP LSAP selector for SyncML over IrOBEX, legal values from 0x01 to 0x6F |

## OBEX Over Bluetooth

The Bluetooth section is specified so that the SyncML client MUST be able to function as either an OBEX client, or an OBEX server, or both. The SyncML server MUST be able to function as both the OBEX server and client.

The figure below shows the protocols when SyncML and OBEX are run over the Bluetooth protocol stack.

Figure 1 OBEX over Bluetooth

The Baseband, LMP, and L2CAP are the OSI layer 1 and 2 Bluetooth protocols. RFCOMM is the Bluetooth adaptation of GSM TS 07.10. SDP is the Bluetooth Service Discovery Protocol [BTSDP].

The SyncML Client layer shown in Figure 1 is the entity providing the sync client agent functionality. The SyncML Server is the SW providing the sync engine functionality.

In this specification, the SyncML client can work either as an OBEX client or as an OBEX server at the OBEX protocol layer. In consequence, the SyncML server can work either as an OBEX client or as an OBEX server. The OBEX role depends on the fact which one, the SyncML client or the SyncML server, initiates sync.

### Bluetooth Service Discovery

To enable the OBEX connection over the Bluetooth protocol stack, the SyncML server MUST advertise and the SyncML client SHOULD advertise service records, which can be retrieved by a connecting device using the Bluetooth SDP [BTSDP].

In the case of the SyncML server, the following information, i.e., service records MUST be put into the SDDB (Service Discovery DataBase).

| Item | Definition: | Type/ Size: | Value: | AttrID: | Status: | Default Value: |
| --- | --- | --- | --- | --- | --- | --- |
| Service Class ID List |  |  | N/A | 0x0001** | MUST |  |
|  | Service Class #0 | SyncMLServer | UUID | * | N/A | MUST |  |
| Protocol Descriptor list |  |  | N/A | 0x0004** | MUST |  |
|  | Protocol ID #0 | L2CAP | UUID | 0x0100** | N/A | MUST |  |
|  | Protocol ID #1 | RFCOMM | UUID | 0x0003** | N/A | MUST |  |
|  | Param #0 | CHANNEL | Uint8 | Varies | N/A | MUST |  |
|  | Protocol ID #2 | OBEX | UUID | 0x0008** | N/A | MUST |  |
| Service name | Displayable Text name | String | Varies | 0x0000+b*** | MAY | “SyncML Server" |

Table 1 SyncML Server Service Records

* The value 00000001-0000-1000-8000-0002EE000002 SHOULD be used in this place.

** The value or the attribute ID is specified in the Bluetooth Assigned Numbers specification [BTAN].

*** ’b’ in this table represents a base offset as given by the LanguageBaseAttributeIDList attribute. For the principal language b MUST be equal to 0x0100 as described in the Bluetooth SDP specification [BTSDP].

The service records, which the SyncML client SHOULD put into its SDDB, are listed below.

| Item | Definition: | Type/ Size: | Value: | AttrID: | Status: | Default Value: |
| --- | --- | --- | --- | --- | --- | --- |
| Service Class ID List |  |  | N/A | 0x0001** | MUST |  |
|  | Service Class #0 | SyncMLClient | UUID | * | N/A | MUST |  |
| Protocol Descriptor list |  |  | N/A | 0x0004** | MUST |  |
|  | Protocol ID #0 | L2CAP | UUID | 0x0100** | N/A | MUST |  |
|  | Protocol ID #1 | RFCOMM | UUID | 0x0003** | N/A | MUST |  |
|  | Param #0 | CHANNEL | Uint8 | Varies | N/A | MUST |  |
|  | Protocol ID #2 | OBEX | UUID | 0x0008** | N/A | MUST |  |
| Service name | Displayable Text name | String | Varies | 0x0000+b*** | MAY | “SyncML Client" |

Table 2 SyncML Client Service Records

* The value 00000002-0000-1000-8000-0002EE000002 SHOULD be used in this place.

** The value or the attribute ID is specified in the Bluetooth Assigned Numbers specification [BTAN].

*** ’b’ in this table represents a base offset as given by the LanguageBaseAttributeIDList attribute. For the principal language b MUST be equal to 0x0100 as described in the Bluetooth SDP specification [BTSDP].

#### SDP Protocol Data Units

Table 3 shows the specified SDP PDUs (Protocol Data Units), which areREQUIRED.

| PDU no. | SDP PDU | Ability to Send | Ability to Retrieve |
| --- | --- | --- | --- |
|  |  | SyncML Client | SyncML Server | SyncML Client | SyncML Server |
| 1 | SdpErrorResponse | MUST* | MUST | MUST** | MUST |
| 2 | SdpServiceSearchAttribute-Request | MUST** | MUST | MUST* | MUST |
| 3 | SdpServiceSearchAttribute-Response | MUST* | MUST | MUST** | MUST |

Table 3 SDP PDUs

* This is only applicable if the SyncML client is able to function as the OBEX server.

** This is only applicable if the SyncML client is able to function as the OBEX client.

### Other Bluetooth Protocol Requirements

This specification partially requires compliance to the Bluetooth Serial Port (SeP) Profile [BTSEP] if Bluetooth is used as a physical medium for OBEX. These are:

- The compliance is REQUIRED to the RFCOMM requirements as defined in Chapter 4 in the SeP Profile.

- The compliance is REQUIRED to the L2CAP requirements as defined in Chapter 5 in the SeP Profile.

- The compliance is REQUIRED to the LM protocol requirements as defined in Chapter 7 in the SeP Profile.

The SDP requirements are defined by this specification and thus, any of the requirements defined in the SeP profile (Chapter 6 in the SeP profile) does not apply to this specification. The SyncML server MUST comply with both the Device 'A' and Device 'B' requirements as defined in the SeP Profile. The SyncML client MUST comply with either the Device 'A' requirements, or with the Device 'B' requirements, or both as defined in the SeP Profile.

The Bluetooth LC (Link Controller) capabilities and The Bluetooth Generic Access Profile (GAP) requirements for this specification are defined in Chapter 6.5 and Chapter 7 of the Bluetooth GOEP [BTGOEP], respectively. The SyncML server MUST comply with both the client and server requirements as defined in Chapter 6.5 and Chapter 7 in the GOEP. The SyncML client MUST comply with either the client requirements, or the server requirements, or both as defined in Chapter 6.5 and Chapter 7 in the GOEP.

# OBEX Mapping to SyncML

The following sections define the requirements for the binding of SyncML to OBEX.

In client initiated sync, the SyncML client initiates the OBEX link, so it is also the OBEX client.  The SyncML client can disconnect the OBEX link when it has received the last sync message from the SyncML server.

With server alerted sync, the SyncML server initiates the OBEX link, so it is the OBEX client. The SyncML server cannot disconnect the OBEX link before it has received the SyncML response message for the last SyncML message including a Sync command that it sends.

## OBEX Operations

The OBEX layer SHOULD be disconnected using the OBEX DISCONNECT operation.   The OBEX specification also allows the link to be disconnected by disconnecting the underlying transport layer.

The OBEX connection can be authenticated as part of the OBEX CONNECT request/response messages, using the authenticate challenge and response headers

The OBEX client MAY send an OBEX ABORT request, to terminate a multi-packet operation (such as PUT) before it would normally end.

The following OBEX operations are REQUIRED for Client Initiated sessions.

| OBEX Operation | SyncML Server / OBEX Server | SyncML Client / OBEX Client |
| --- | --- | --- |
| Connect | MUST | MUST |
| Disconnect | MUST | MUST |
| Put | MUST | MUST |
| Get | MUST | MUST |
| Abort | MUST | MAY |

The following OBEX operations are REQUIRED for Server Initiated sessions.

| OBEX Operation | SyncML Server / OBEX Client | SyncML Client / OBEX Server |
| --- | --- | --- |
| Connect | MUST | MUST |
| Disconnect | MUST | MUST |
| Put | MUST | MUST |
| Get | MUST | MUST |
| Abort | MAY | MUST |

## OBEX Connection Overview

The OBEX connection is made at the start of the synchronization, and remains open until the synchronization has completed.

The following example shows the creation of an OBEX connection, the mapping of PUT and GET requests to the SyncML message transfers, and the OBEX disconnection.

This example is not intended to show a complete a SyncML Session but merely illustrates the use of PUT and GET within a SyncML OBEX binding implementation.

| OBEX Client | OBEX Server | Message Direction |
| --- | --- | --- |
| CONNECT Request |  |  |
|  | Success Response |  |
| PUT Request |  | SyncML Message from |
|  | Continue Response | OBEX Client to OBEX Server |
| PUT Request … |  |  |
|  | Continue Response … |  |
| PUT Final Request |  |  |
|  | Success Response |  |
| GET Request |  | SyncML Message from |
|  | Continue Response | OBEX Server to OBEX Client |
| GET Request … |  |  |
|  | Continue Response … |  |
| GET Final Request |  |  |
|  | Success Response |  |
| DISCONNECT Request |  |  |
|  | Success Response |  |

### Multiple Messages Per Package

Each SyncML message MUST be transferred as a SyncML MIME media type within the body of the OBEX request or response. However in order to transfer the message the OBEX / transport layer MAY split the message into many PUT requests, followed by a PUT Final Request. When there are multiple SyncML messages per SyncML package to transfer, each message is transferred in a separate 'set' of PUT/GET commands; depending on whether it is a SyncML request or response.

The recipient of a SyncML message can determine if there are more SyncML messages in the package by the absence of the Final element in the last received SyncML message. When the recipient receives a SyncML message with the Final element, it is the final message within that SyncML package.

Similarly if the PUT is not a PUT final then the recipient knows it is not the final part of the SyncML message, or if the response to the GET Final Request is not an OK/success then there is more data still to transfer.

### Type header requirement

Data synchronization client implementations conforming to this specification MUST support the Type header with either the "application/vnd.syncml+xml" or "application/vnd.syncml+wbxml" MIME media type values. Data synchronization server implementations conforming to this specification MUST support both "application/vnd.syncml+xml" and "application/vnd.syncml+wbxml" MIME media type values, as requested by the SyncML data synchronization client.

Device Management client implementations conforming to this specification MUST support this header with either the "application/vnd.syncml.dm+xml" or "application/vnd.syncml.dm+wbxml" MIME media type values. Device management server implementations conforming to this specification MUST support both "application/vnd.syncml.dm+xml" and "application/vnd.syncml.dm+wbxml" MIME media type values, as requested by the SyncML device management client.

In the case of Server Alerted Notification, the Type header of the OBEX packet transferring the notification package MUST include the MIME media type, "application/vnd.syncml.notification" for Device Management usage for the Server Alerted Notification package as defined in [SAN] and "application/vnd.syncml.ds.notification" for Data Synchronization usage.

## OBEX Connection Establishment

The OBEX connection is established by the SyncML application generating a Connect Request, and the remote device indicates that the connection has been established, by returning a Connect Response. For each SyncML session, a separate OBEX connection MUST be established.

The OBEX CONNECT request packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Opcode for CONNECT | 0x80 | M |  |
| Field | Packet Length | Varies | M |  |
| Field | OBEX Version Number | 0x10 | M | In [OBEX] it is stated that current version is 1.0 |
| Field | Flags | Varies | M |  |
| Field | Max OBEX Packet Length | Varies | M |  |
| Header | Target | Varies | M | The UUID to be used in data synchronization is SYNCML-SYNC and in device management is SYNCML-DM. |

The OBEX CONNECT response packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Response code for CONNECT request | 0x0A | M | 0xA0 for success, otherwise fail |
| Field | Packet Length | Varies | M |  |
| Field | OBEX Version Number | 0x10 | M | In [OBEX] it is stated that current version is 1.0 |
| Field | Flags | Varies | M |  |
| Field | Max OBEX Packet Length | Varies | M |  |
| Header | Connection ID | Varies | M | Connection ID is set by the Server during the OBEX Connect operation as a shorthand way for the client to direct the requests. This MUST be the first header. |
| Header | Who | Varies | M | The UUID returned is the same UUID that was sent in the connect request target header |

## Exchanging SyncML Data over the OBEX Connection

Once an OBEX connection has been established, SyncML data can be transferred over the link.

The OBEX PUT request packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Opcode for PUT | 0x02 or 0x82 | M | 0x02 is used for packets previous to the last put packet. 0x82 (which is 0x02 with the high bit set) is used for the last put packet. |
| Field | Packet Length | Varies | M |  |
| Header | Connection ID | Varies | M | Connection ID is set to the value returned by the Server during the OBEX Connect operation. This MUST be the first header. Sent only once in first packet in the request sequence. |
| Header | Type | Varies | M | The MIME type of the object. This MUST contain the SyncML MIME type declaration. Sent only once in first packet in the request sequence, MUST precede object Body headers. |
| Header | Length | Varies | O | Length of the object. This header is OPTIONAL but highlyRECOMMENDED. Sent only once in the request sequence. |
| Header | Body/End of Body | Varies | M | End of Body identifies the last chunk of the object body. End of Body header (PUT final packet) SHOULD be sent with an empty body. |

The OBEX PUT response packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Response code for PUT | 0x90, 0xAO, 0xCD, 0xCF, … | M | 0x90 for continue 0xA0 for success 0xCD if the object is too large 0xCF if the object type is not supported |
| Field | Packet Length | Varies | M |  |

Other headers, which can be optionally used, are found in [OBEX]

The OBEX GET request packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Opcode for GET | 0x03 or 0x83 | M | 0x03 is used for packets previous to the last packet containing headers. 0x83 (which is 0x03 with the final bit set) is used for the last packet containing headers and for subsequent get packets in the current Get request sequence without headers. No headers can be sent in Get request packets once the 0c83 has been sent in a previous packet. |
| Field | Packet Length | Varies | M |  |
| Header | Connection ID | Varies | M | Connection ID is set to the value returned by the Server during the OBEX Connect operation. This MUST be the first header. Sent only once in first packet in the request sequence. |
| Header | Type | 0x42, … | M | The MIME type of the object. This MUST contain the SyncML MIME type declaration. Sent only once in first packet in the request sequence. |

The OBEX GET response packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Response code for GET | 0x90, 0xAO, 0xC0, 0xC3, … | M | 0x90 for continue 0xA0 for success 0xC0 bad request 0xC3 forbidden |
| Field | Packet Length | Varies | M |  |
| Header | Length | 0xC3, … | O | Length of the object. This header is OPTIONAL but highlyRECOMMENDED. Sent only once in the request sequence. |
| Header | Body/End of Body | 0x48/0x49, … | M | End of Body identifies the last chunk of the object body. |

Other headers, which can be optionally used, are found in [OBEX]

## OBEX Disconnection

The OBEX connection is disconnected by the SyncML application, generating a Disconnect Request, and the remote device indicates that the connection has been terminated, by returning a success Response.

The OBEX DISCONNECT request packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Opcode for DISCONNECT | 0x81 | M |  |
| Field | Packet Length | Varies | M |  |
| Header | Connection ID | Varies | M | Connection ID is set to the value returned by the Server during the OBEX Connect operation. This MUST be the first header. |

Other headers (such as Description) which can be optionally used are found in [OBEX] .

The OBEX DISCONNECT response packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Response code for DISCONNECT | 0xAO | M | 0xA0 for success, otherwise fail |
| Field | Packet Length | Varies | M |  |

## OBEX ABORT

The client can send an OBEX abort request to terminate a multi-packet operation (such as PUT) before it would normally end. The ABORT request and response always fit in one OBEX packet, and they always have the Final bit set.

The OBEX ABORT request packet contains the following fields and headers:

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Opcode for ABORT | 0xFF | M |  |
| Field | Packet Length | Varies | M |  |
| Header | Connection ID | Varies | O | Connection ID is set to the value returned by the Server during the OBEX Connect operation. This MUST be the first header if it is included. |

Other headers (such as Description) which can be optionally used are found in [OBEX] .

The OBEX ABORT response packet contains the following fields and headers.

| Field/ Header | Name | Value | M/O | Explanation |
| --- | --- | --- | --- | --- |
| Field | Response code for ABORT | 0xAO | M | 0xA0 for success, otherwise fail and the client SHOULD disconnect the OBEX connection. |
| Field | Packet Length | Varies | M |  |

Other headers (such as Description) which can be optionally used are found in [OBEX] .

## Server Alerted Notification

The OBEX connection is established by the SyncML server generating a CONNECT Request. The OBEX CONNECT request MUST have as the Target header the UUID of SYNCML-SYNC for a Data Synchronization packages and a UUID of SYNCML-DM for Device Management packages. Once an OBEX connection has been established the Server Alerted Notification package data can be transferred over the link.

# Examples

The following examples are formatted as the examples in [OBEX] .

## OBEX Connect Example

| Client Request: | Bytes | Meaning |
| --- | --- | --- |
| Opcode | 0x80 | CONNECT, Final bit set |
|  | 0x0015 | packet length = 21 |
|  | 0x10 | version 1.0 of OBEX |
|  | 0x00 | flags, all zero for this version of OBEX |
|  | 0x0200 | 512 bytes is the max OBEX packet size client can accept |
|  | 0x46 | HI for Target header |
|  | 0x000E | Length of Target header |
|  | 0x53594E434D4C | UUID for SyncML DS (“SYNCML-SYNC”) |
|  | 2D53594E43 |  |
| Server Response: |  |  |
| response code | 0xA0 | SUCCESS, Final bit set |
|  | 0x001A | packet length of 26 |
|  | 0x10 | version 1.0 of OBEX |
|  | 0x00 | Flags |
|  | 0x0200 | 1K max packet size |
|  | 0xCB | HI for Connection Id header |
|  | 0x00000001 | ConnId = 1 |
|  | 0x4A | Who HI |
|  | 0x000E | Length of Who Header |
|  | 0x53594E434D4C 2D53594E43 | UUID of responding application (same value as Target header in request (“SYNCML-SYNC”) |

## OBEX Disconnect Example

| Client Request: | bytes | Meaning |
| --- | --- | --- |
| opcode | 0x81 | DISCONNECT, Final bit set |
|  | 0x0008 | packet length = 8 |
|  | 0xCB | HI for Connection Id header |
|  | 0x00000001 | ConnId = 1 |
| Server Response: |  |  |
| response code | 0xA0 | SUCCESS, Final bit set |
|  | 0x0003 | packet length = 3 |

## OBEX Abort Example

| Client Request: | bytes | Meaning |
| --- | --- | --- |
| opcode | 0xFF | ABORT, Final bit set |
|  | 0x0008 | packet length = 8 |
|  | 0xCB | HI for Connection Id header |
|  | 0x00000001 | ConnId = 1 |
| Server Response: |  |  |
| response code | 0xA0 | SUCCESS, Final bit set |
|  | 0x0003 | packet length = 3 |

## OBEX Put Example

| Client Request: | Bytes | Meaning |
| --- | --- | --- |
| opcode | 0x02 | PUT, Final bit not set |
|  | 0x0200 | 512 bytes is length of packet |
|  | 0xCB | HI for Connection Id header |
|  | 0x00000001 | ConnId = 1 |
|  | 0x42 | HI for Type header |
|  | 0x0020 | Length of Type header |
|  | 0x6170706C6963 6174696F6E2F76 6E642E73796E63 6D6C2B7762786D 6C00 | Type of object (application/vnd.syncml+wbxml) (null terminated ASCII text) |
|  | 0xC3 | HI for Length header |
|  | 0x000004FE | Length of object is 1278 bytes |
|  | 0x48 | HI for Object Body chunk header |
|  | 0x01D3 | Length of Body header = 467. 464 plus HI and header length |
|  | 0x.......... | 464 bytes of body |
| Server Response: |  |  |
| response code | 0x90 | CONTINUE, Final bit set |
|  | 0x0003 | length of response packet |
| Client Request: |  |  |
| opcode | 0x02 | PUT, Final bit not set |
|  | 0x0200 | 512 bytes is length of packet |
|  | 0x48 | HI for Object Body chunk |
|  | 0x01FD | Length of Body header = 509. 506 plus HI and header length |
|  | 0x.......... | next 506 bytes of body |
| Server Response: |  |  |
| response code | 0x90 | CONTINUE, Final bit set |
|  | 0x0003 | length of response packet |
| Client Request: |  |  |
| opcode | 0x82 | PUT, Final bit set |
|  | 0x013A | 314 bytes is length of packet |
|  | 0x49 | HI for Object End-of-Body chunk |
|  | 0x0137 | Length of header = 311. 308 plus HI and header length |
|  | 0x.......... | last 308 bytes of body |
| Server Response: |  |  |
| response code | 0xA0 | SUCCESS, Final bit set |
|  | 0x0003 | length of response packet |

## OBEX Get Example

| Client Request: | bytes | Meaning |
| --- | --- | --- |
| opcode | 0x83 | GET, Final bit set |
|  | 0x0028 | 40 bytes is length of GET packet |
|  | 0xCB | HI for Connection Id header |
|  | 0x00000001 | ConnId = 1 |
|  | 0x42 | HI for Type header |
|  | 0x0020 | Length of Type header |
|  | 0x6170706C6963 6174696F6E2F76 6E642E73796E63 6D6C2B7762786D 6C00 | Type of object (application/vnd.syncml+wbxml) (null terminated ASCII text) |
| Server Response: |  |  |
| Response code | 0x90 | CONTINUE, Final bit set |
|  | 0x0200 | length of response packet |
|  | 0xC3 | HI for Length header |
|  | 0x000002BE | Length of object is 702 bytes |
|  | 0x48 | HI for Object Body chunk |
|  | 0x01F8 | Length of header = 504. 501 plus HI and header length |
|  | 0x.......... | 501 bytes of body |
| Client Request: | bytes | Meaning |
| opcode | 0x83 | GET, Final bit set |
|  | 0x0003 | 3 bytes is length of GET packet |
| Server Response: |  |  |
| Response code | 0xA0 | SUCCESS, Final bit set |
|  | 0x0038 | length of response packet |
|  | 0x49 | HI for End-of-Body chunk |
|  | 0x00CC | Length of header = 204. 201 plus HI and header length |
|  | 0x.......... | last 201 bytes of body. |

Change History	(Informative)

Approved Version History

| Reference | Date | Description |
| --- | --- | --- |
| OMA-SyncML-OBEXBinding-V1_1_2-20030612-A | 12 Jun 2003 | Initial OMA release |
| OMA-TS-SyncML_OBEXBinding-V1_2-20070221-A | 21 Feb 2007 | Status changed to Approved by TP: OMA-TP-2007-0005R03-INP_ERP_SyncML_Common_V1_2_for_Final_Approval |

Static Conformance Requirements	(Normative)

The notation used in this appendix is specified in Error! Reference source not found..  The static conformance requirements are specified for Client Initiated and Server Initiated Sessions.

Client Features

Common SCRs – OBEX Session Requirements

The following OBEX operations are REQUIRED for all sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-C-001 | Support for OBEX Connect operation | 6.1 | M |  |
| DSDM-OBEX-C-002 | Support for OBEX Disconnect operation | 6.1 | M |  |
| DSDM-OBEX-C-003 | Support for OBEX Put operation | 6.1 | M |  |
| DSDM-OBEX-C-004 | Support for OBEX Get operation | 6.1 | M |  |

SCRs for Client Initiated Sessions

The following OBEX operations are REQUIRED for Client Initiated sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-C-005 | SyncML Client/OBEX Client support for OBEX Abort operation | 6.1 | O |  |

SCRs for Server Initiated Sessions

The following OBEX operations are REQUIRED for Server Initiated sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-C-006 | SyncML Client/OBEX Server support for OBEX Abort operation | 6.1 | M |  |

Server Features

Common SCRs

The following OBEX operations are REQUIRED for all sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-S-001 | Support for OBEX Connect operation | 6.1 | M |  |
| DSDM-OBEX-S-002 | Support for OBEX Disconnect operation | 6.1 | M |  |
| DSDM-OBEX-S-003 | Support for OBEX Put operation | 6.1 | M |  |
| DSDM-OBEX-S-004 | Support for OBEX Get operation | 6.1 | M |  |

SCRs for Client Initiated Sessions

The following OBEX operations are REQUIRED for Client Initiated sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-S-005 | SyncML Server/OBEX Server support for OBEX Abort operation | 6.1 | M |  |

SCRs for Server Initiated Sessions

The following OBEX operations are REQUIRED for Server Initiated sessions.

| Item | Function | Ref. | Status | Requirement |
| --- | --- | --- | --- | --- |
| DSDM-OBEX-S-006 | SyncML Server/OBEX Client support for OBEX Abort operation | 6.1 | O |  |